Baby42
A simple RISC processor
Jecel Mattos de Assumpção Jr
August 2022

---
name
- 4 bytes (32 bits) of data with 2 bytes of instruction
- And:
The Manchester Baby (Small-Scale Experimental Machine – SSEM) ran a stored memory program in June 1948

---
state
General purpose registers
Program Counter
  31 24 23 16 15 8 7 0
  31 24 23 16 15 8 7 0
r15
r14
r13
r12
r11
r10
r9
r8
r7
r6
r5
r4
r3
r2
r1
r0
17 words = 68 bytes = 136 hexadecimal digits
    + external memory
Manchester Baby: 3 registers
     + 32 words of memory of 32 bits each

---
RISC style
Two instruction formats:
- Data manipulation instructions only operate on registers, or a register and an immediate value present in the instruction itself
- Data storage transfer a register to/from memory (jump and link has the same format, though it should be considered a third kind of instruction)

---
RISC: how many instructions?
- Counting all variations in assembly syntax we have 106 standard instructions and 12 optional ones (multiplication)
- Not counting the variations we have 30 standard instructions and 3 optional ones
- The control unit deals with only five instruction types:
  1. ALU (Math, Logic and Multiply)
  2. Comparison
  3. Load
  4. Store
  5. Jump and Link

---
Data Manipulation Instructions
15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0
d
s
0
K
#
Second operand
cascade
immediate
operation code
First operand and destination
30 of the 32 possible op codes are used, but due to # and K nearly all instructions have 4 variations.
The assembly language syntax is C-like, with an addition being
indicated by
    rD += rS

---
# - Immediate values
"immediate" changes the second operand to be a number from
-6 to 7 instead of a register. The value -7 (9 in hex) indicates that the
actual operand is the next 32 bits and -8 (8 in hex) indicates 16 bits
In assembly, a # character is placed before the second operand
to indicate that it is an immediate. Otherwise the numbers 0 to
15 indicate a register.

---
K - Cascade
"cascade" changes the destination to be the first operand of the following instruction. A sequence like
    r3 <<= #2 ; multiply by four
    r3 += r1
can be implemented with cascade as
    r5 = {r3 << #2} + r1
Unlike the original code fragment, these two instructions don't destroy the value in r3. So though the architecture is a two address in general, it can have the functionality of three addresses (actually four) when needed. The second instruction's syntax is changed from "d op= s" to "d = {..} op s" and the cascaded instruction is placed in the curly brackets also in infix form. It is possible to have more than one level of cascade, but then the d field of intermediate instructions is wasted.

---
Math: op code is 0 0+!C
- + means that the destination is added to the source
- ! means that the source is bitwise inverted (one’s complement)
- C means that the
 carry in is set

---
Math
1?ds
0?ds
2?ds
3?ds
?0ds
move	d = s	d = #s
increment	d = s+1	d = #s+1
invert	d = !s	d = !#s
negate	d = ~s	d = ~#s
add	d += s	d += #s	{d + s}	{d + #s}
add forcing carry	d += s+1	d += #s+1	{d + s+1}	{d + #s+1}
subtract forcing borrow	d -= s-1	d -= #s-1	{d - s-1}	{d - #s-1}
subtract	d -= s	d -= #s	{d - s}	{d - #s}
?1ds
?2ds
?3ds
?4ds
?5ds
?6ds
?7ds

---
Logic: op code is 0 1&!M
- & means an AND operation, otherwise it is an OR
- ! means that output is bitwise inverted (one’s complement)
- M means a
modified version
of the instruction

---
Logic (the 4 bits are !s!d s!d !sd sd)
1?ds
0?ds
2?ds
3?ds
?8ds
0111 or	d |= s	d |= #s	{d | s}	{d | #s}
0110 exclusive or	d ^= s	d ^= #s	{d ^ s}	{d ^ #s}
1000 nor	d !|= s	d !|= #s	{d !| s }	{d !| #s}
1001 equivalence	d !^= s	d !^= #s	{d !^ s}	{d !^ #s}
0001 and	d &= s	d &= #s	{d & s}	{d & #s}
0010 and invert	d &!= s	d &!= #s	{d &! s}	{d &! #s}
1110 nand	d !&= s	d !&= #s	{d !& s}	{d !& #s}
1101 nand invert	d !&!= s	d !&!= #s	{d !&! s}	{d !&! #s}
?9ds
?Ads
?Bds
?Cds
?Dds
?Eds
?Fds

---
Logic: remaining rules
10d0 d = #0
00dd d = d
2Edd 0Cds d = {d !& d) & s
00ds d = s
02ds d = !s
2Edd 0Eds d = {d !& d) !& s
02dd d = !d
10dF d = #-1
0000 clear
0011 destination
0100 other and invert
0101 source
1010 not source
1011 other nand invert
1100 not destination
1111 set

---
Shift: op code is 1 00$<
5?ds
4?ds
6?ds
7?ds
?0ds
shift right	d >>= s	d >>= #s	{d >> s}	{d >> #s}
shift left	d <<= s	d <<= #s	{d << s}	{d << #s}
signed shift right	d $>>= s	d $>>= #s	{d $>> s}	{d $>> #s}
rotate left	d <>= s	d <>= #s	{d <> s}	{d <> #s}
?1ds
?2ds
?3ds
Barrel shifter: x[63:0] << a[4:0]
    z0[63:0] = a[0] ? {x[62:0],0} : x
    z1[63:0] = a[1] ? {z0[61:0],2{0}} : z0
    z2[63:0] = a[2] ? {z1[59:0],4{0}} : z1
    z3[63:0] = a[3] ? {z2[55:0],8{0}} : z2
    z[63:0] = a[4] ? {z3[47:0],16{0}} : z3
a = “<” ? s : 32-s
x = (“$” & !“<”) & 32{d[31]}
z[63:0] = {x, d} << a
result = (z[31:0] & “<”) | (z[63:32] & !(!”$” & “<”))

---
Multiply (optional)
5?ds
4?ds
6?ds
7?ds
?4ds
multiply high	d *= s	d *= #s	{d * s}	{d * #s}
multiply low	d *>= s	d *>= #s	{d *> s}	{d *> #s}
multiply signed high	d $*= s	d $*= #s	{d $* s}	{d $* #s}
?5ds
?6ds
?7ds
signed
unsigned
4 bit examples with 8 bit result:
hex (decimal)
    4 (4)
x F (15)
-----
  3C (60)
    C (12)
x F (15)
------
   B4 (180)
    4 (4)
x F (-1)
------
   FC (-4)
    C (-4)
x F (-1)
------
   04 (4)

---
Comparison (calculation)
Greater than d-s ==> !z&c
Equal
d-s ==> z
Greater than or equal d-s ==> c
Not equal
d-s ==> !z
Carry on add
d+s ==> c
Signed greater than d-s ==> !z&(n!^v)
Signed greater than or equal d-s ==> n!^v
c = result[32]
z = !(|\result)
n = result[31]
v = (n&!d[31]&!s[31]) | (!n&d[31]&s[31])

---
Comparison
5?ds
4?ds
6?ds
7?ds
?8ds
Greater than	d > s ? ….	d > #s ? ….	{d > s}	{d > #s}
Greater or equal	d >= s ? ….	d >= #s ? ….	{d >= s}	{d >= #s}
Signed greater than	d $> s ? ….	d $> #s ? ….	{d $> s }	{d $> #s}
Signed greater or equal	d $>= s ? ….	d $>= #s ? ..	{d $>= s}	{d $> #s}
Equal	d == s ? ….	d == #s ? ….	{d == s}	{d == #s}
Not equal	d != s ? ….	d != #s ? ….	{d != s}	{d != #s}
Carry on add	d ++ s ? ….	d ++ #s ? ….	{d ++ s}	{d ++ #s}
?9ds
?Ads
?Bds
?Cds
?Dds
?Eds
?Fds

---
Comparison (trivia)
The comparison instructions will produce a 0 or a 1 result for the next instruction when cascade is used or will skip the next instruction in the normal case when the comparison fails (note that d is not modified)
Note that a comparison that wants less than results can use greater than and swap the operands. This doesn't work if the second operand is an immediate value, but since "if (r3<200) x1 else x2" does the same thing as "if (r3>=200) x2 else x1" it is normally not a problem.
The “d >= s” instruction can be used as a “borrow on subtract” to complement the “d ++ s” (carry on add) instruction.

---
Data Storage Instructions
15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0
b
s
1
#
t
Register to transfer
Second operand
operation code
First operand
immediate
Store	8tbs	b[s] = t	9tbs	b[#s] = t
Load	Atbs	t = b[s]	Btbs	t = b[#s]
Jump and Link	Ctbs	====> b[s]/t	Dtbs	====> b[#s]/t
	E???		F???

---
Load/Store
The address of the memory operation will be the sum of b and s (unless b is 0, in this case it will be just s and the "b" can be omitted):
8t0s [s] = t
9t0s [#s] = t
At0s t = [s]
Bt0s t = [#s]
This allows access to global variables and i/o ports without having to use up a register for the base.

---
Jump and Link
In the case of JL the t register will hold the previous value of the PC (unless t is 0, in which case the old value of the PC is discarded. "/t" can be omitted):
C0bs ====> b[s]
D0bs ====> b[#s]
The new value of the PC will be the sum of b and s (unless b is 0, in this case it will be the sum of s and the previous value of the PC or just the PC if s is a 32 bit constant. The "b" can be omitted):
Ct0s ====> [s]/t
Dt0s ====> [#s]/t
C00s ====> [s]
D00s ====> [#s]
Syntatic sugar for the assembler allows "====> label" and "====> label/t" to be written in place of "====> [#label-.]" and "====> [#label-.]/t" respectively.

---
Bytes: Store byte instruction
       ; code to load a byte from memory
Loadb:
; r1 is the address
; r2 is the destination
; r3 is scratch
r2 = r1[#0]
r3 = {r1 & #3} << #3
r2 = {r2 >> r3} & #255
       ; code to store a byte to memory
Storeb:
; r1 is the address
; r2 is the byte to be stored
; r3 and r4 are scratch
r4 = r1[#0] ; previous word
r3 = {r1 & #3} << #3
r2 &= #255 ; make sure it is a byte
r5 = #255
r5 <<= r3
r4 &~= r5 ; clear destination byte
r4 = {r2 << r3} | r4
r1[#0] = r4
This isn’t too bad. If we redefine load to rotate the word it read on a non aligned address then just two instructions would be needed:
We could define the remaining data storage instruction to be a store byte:
       ; code to load a byte from memory
Loadb:
r2 = r1[#0] ; might be rotated
r2 &= #255
       ; code to store a byte to memory
Storeb:
r1[#0] B= r2

---
Interrupts
The focus in this design is simplicity, even at a cost in performance. Nearly all functionality is implemented in the external interrupt controller. An “irq” signal goes to the processor and an “iack” signal goes back to the controller.
The controller has a visible register for each interrupt level it can handle plus two extra ones for the non existing “level 0” and “level 1” (L0 and L1). The value of these registers is the address for the corresponding handler routine.
When some interrupt is pending the controller raises irq until the processor executes an iack cycle. The cycle looks like a memory read where the address is the value of the next PC (which is stored in L1) and the data read is the value to be loaded into the PC. Interrupts do no nest so even if a new, higher level request arrives it won’t do anything until the current handler returns.

---
Return from Interrupt
While register L1 holds the address saved during the iack cycle, L0 has a constant value in bits 16 to 31 such that a jump to $ircontroller+2 will execute a jump back to the user program.
When bit 0 of L0 is set interrupts are disabled. This happens automatically in an iack cycle and is cleared on a fetch from $ircontroller+2, but can also be set or cleared by software to create a protected region. Bit 1 is always 0 while bits 2 to 15 are set if interrupt levels 2 to 15, respectively, are pending. Levels beyond 15 can exist, but register L0 can’t be used to check on them.
Bit 0 of L2, L3, L4, etc must be cleared for interrupts at that level to be accepted. This will happened if they hold a valid address since instructions are aligned on even bytes. On reset bit 0 of all registers are set.
Note that while the interrupt controller saves the user’s PC, any other registers must be explicitly saved and then restored before the return.

---
Assembly Language Expressions
Numeric literals are always integers represented by a sequence of digits, optionally separated by underscores to make them more readable. The size depends on the context in which the expression is used. Though there is a default radix, any number literal can specify its representation by starting with the value of the highest digit in the base (radix), followed by a “$” character and then followed by the actual digits.
We can have binary numbers like 1$1101_1001, decimal numbers like 9$42, hexadecimal numbers like F$4AC0 or even octal numbers like 7$1776. The digits after “9” are “A” to “Z” (lower case is equivalent to upper case).
Defined symbols are treated as their values.
The operations are, in order of highest to lowest precedence: *, /, % then +, - then <<, >>, $>>, <> then & then ^ then |. Parenthesis override the precedence and must be used inside cascades so the top level operator is the instruction.

---
Assembly language directives:
define
Symbols can be defined by
    name: expression
A period character in an expression indicates the value of the PC for that instruction. An empty expression is equivalent to just a period, so is equivalent of defining a label in other assemblers. This means that labels must be on a line of their own instead of coming before an instruction.
If a symbol is defined more than once, only the last definition is used in the whole program and a warning is issued.
Registers in an assembly instruction are just expressions that evaluate from 0 to 15 (0 to 7 in Baby042) so besides the default names r0 to r15 more meaningful names can be defined.

---
Assembly language directives:
configuration
Symbol names starting with “$” are an error, unless they are in the list below and set to one of the indicated values. In that case they change the configuration of the assembler and/or the simulator.
Symbol	Valid Values	Default	Description
$processor	42, 22, 18	42	Baby42, Baby22 or Baby042 (9$18=7$42)
$radix_dump	1$1 to Z$Z	F$F	Base of numbers in addresses and data
$radix_source	1$1 to Z$Z	9$9	Base of numbers in the source code
$vresolution	0, 192, 384, 768	192	No video, 256x192, 512x386 or 1024x768
$colorbits	1, 6, 12, 24	6	B&W, EGA, NeXT color, True Color

---
Assembly language directives:
configuration (continued)
Symbol	Valid Values	Default	Description
$framebuffer	Multiple of $fboffset	F$FFFF_4000	Where the video bitmap starts
$fboffset	8KB, 16KB, 32KB, 64KB, 128KB, 256KB, 512KB, 1MB	16KB	Power of 2 larger than 1/3 of the bitmap size
$ircontroller	Word aligned	F$FFFF_FF00	Where the interrupt level registers are

---
Assembly language directives:
include file
A line can be replaced with the contents of another file with:
    < “file name”
As the assembler generates a single output and doesn’t use a linker, the only way to develop with multiple files is to include the others into a top file. The tools can optionally show the contents of the file right below the directive adding “> “ to each line. With multiple levels of include you can easily have lines starting with “> > > “ or similar.

---
Assembly language directives:
origin
The value of the PC can be changed with
    % expression
This is equivalent of "org" in other assemblers. If 120 bytes need to be allocated, then "% .+120" will do the job.
Instructions should always be aligned on an even byte. This expression
can force that to be the case:
    % ((.+1)/2)*2

---
Assembly language directives:
constants
Constants can be inserted into the instruction stream with
    # expr1, expr2, expr3, B# expr4, expr5, H# expr6, # expr7, expr8
The # interprets the following expressions as 32 bit values, while B# inserts 8 bit values and H# 16 bit values.
Placing ASCII characters between two " has the same effect as B# followed by the list of the characters' numeric value.

---
Example 1
Jan Gray used this simple C program to illustrate the assembly language of his XR16 processor (http://www.fpgacpu.org/papers/xsoc-series-drafts.pdf)
typedef struct TN {
  int k;
  struct TN *left, *right;
} *T;
T search(int key, T p) {
  while (p && p->k != key)
    if (p->k < key)
      p = p->right;
    else
      p = p->left;
    return p;
}

---
        ; Example 1 Baby42 machine language and assembly with LCC style
        k: 0
        left: 4
        right: 8
        search: ; r3=key r4=p r9=scratch r2=return
D008 000E ====> L3
        L2:
B940 r9 = r4[#k]
4893 D006 r9 > r3 ? ====> L5
B448 0008 r4 = r4[#right]
D002 ====> L6
        L5:
B444 r4 = r4[#left]
        L6:
        L3:
0094 r9 = r4
5C90 D008 0008 r9 == #0 ? ====> L7
B940 r9 = r4[#k]
4D93 D008 FFE2 r9 != r3 ? ====> L2
        L7:
0024 r2 = r4
        L1:
D0D0 ====> r13[#0] ; return address was in r13

---
        ; Example 1 Baby42 machine language and assembly with better compiler
        ; that optimizes jumps to jumps and jumps to returns
        k: 0
        left: 4
        right: 8
        search: ; r3=key r4=p r9=scratch r4=return value
5C90 D0D0 r4 == #0 ? ====> r13[#0] ; return
B940 r9 = r4[#k]
5C93 D0D0 r9 == r3 ? ====> r13[#0]
4893 D008 0008 r3 > r9 ? ====> L5
B448 0008 r4 = r4[#right]
D008 FFE8 ====> search
        L5:
B444 r4 = r4[#left]
D008 FFE2 ====> search

---
Example 2
Here is the famous Sieve of Eratosthenes benchmark published in Byte magazine:
1 SIZE = 8190
2 DIM FLAGS(8191)
3 PRINT "Only 1 iteration"
5 COUNT = 0
6 FOR I = 0 TO SIZE
7 FLAGS (I) = 1
8 NEXT I
9 FOR I = 0 TO SIZE
10 IF FLAGS (I) = 0 THEN 18
11 PRIME = I+I + 3
12 K = I + PRIME
13 IF K > SIZE THEN 17
14 FLAGS (K) = 0
15 K = K + PRIME
16 GOTO 13
17 COUNT = COUNT + 1
18 NEXT I
19 PRINT COUNT," PRIMES"

---
        size: 8190
        true: r10
        false: r11
        flags: r12
        flg:
???? .. ?? % .+8191
        count: r1
        i: r2
        prime: r3
        k: r4
        text1:
  4F 6E6C "Only 1 iteration", B# 0
7920 3120
6974 6572
6174 696F
6E00
        text2:
2050 5249 " PRIMES", B# 0
4D45 5300
        sieve:
10C0 flags = #flg
10A1 true = #1
10B0 false = #0
1008 1FFF r0 = #text1
DD08 ???? ====> PrintText/r13
        ; library subroutine expects
        ; return address in r13
1010 count = #0
1020 i = #0
        for1:
5828 1FFE i > #size ? ====> endfor1
D008 0008
8AC2 flags[i] = true
1421 i += #1
D008 FFF0 ====> for1
        endfor1:
1020 i = #0
        for2:
5828 1FFE i > #size ? ====> endfor2
D008 0028
A5A2 r5 = flags[i]
5C50 D008 r5 == #0 ? ====> L18
001A
2422 1433 prime = {i+i} + #3
2423 1440 k = {i + prime} + #0

---
        L13:
5848 1FFE k > #size ? ====> L17
D008 0008
8BA4 flags[k] = false
0443 k += prime
D008 FFF0 ====> L13
        L17:
1411 count += #1
        L18:
1421 i += #1
D008 FFD0 ====> for2
        endfor2
0001 r0 = count
DD08 ???? ====> PrintInt/r13
1008 2010 r0 = #text2
DD08 ???? ====> PrintText/r13
D008 ???? ====> Stop
There is also a C version of the benchmark in the Wikipedia article
(https://en.wikipedia.org/wiki/Byte_Sieve). But Basic, specially a version as primitive as this, corresponds a lot more directly to the assembly language implementation.
Normally code that calls other subroutines should save the return address on the stack, but in this case we end with a jump instead of a return.
Since the address of flags happens to be 0 (it is a byte pointer), it would be possible to use "i[#FLG]" in the load and store instructions instead of "flag[i]", which would save one register. But that is not something that would normally happen, so it wasn't used in this example either.

---
Example 3: ARM and Baby42
AREA LOG, CODE, READONLY
EXPORT log
; r0 = input variable n
; r0 = output variable m (0 by default)
; r1 = output variable k (n <= 2^k)
Log
MOV r2, #0 ; set m = 0
MOV r1, #-1 ; set k = -1
log_loop
TST r0, #1 ; test LSB(n) == 1
ADDNE r2, r2, #1 ; set m = m+1 if true
ADD r1, r1, #1 ; set k = k+1
MOVS r0, r0, LSR #1 ; set n = n>>1
BNE log_loop ; continue if n != 0
CMP r2, #1 ; test m ==1
MOVEQ r0, #1 ; set m = 1 if true
log_rtn
MOV pc,lr
END
; AREA LOG, CODE, READONLY
; EXPORT log
; r0 = input variable n
; r0 = output variable m (0 by default)
; r1 = output variable k (n <= 2^k)
Log:
r2 = #0 ; set m = 0
r1 = #-1 ; set k = -1
log_loop:
{r0 & #1) == #1 ? r2 += #1 ; test LSB(n) == 1
        ; set m = m+1 if true
r1 += #1 ; set k = k+1
r0 >>= #1 ; set n = n>>1
r0 != #0 ? ====>log_loop ; continue if n != 0
r2 == #1 ? r0 = #1 ; test m ==1
        ; set m = 1 if true
log_rtn:
====>[lr]
40 bytes, hence Thumb
26 bytes

---
What is missing?
- No floating point math
- No exceptions (if the missing op codes are defined as either NOPs or redundant)
- No MMU (memory management unit) or supervisor mode
- No debug interface (JTAG or control panel)

---
Variation 1: baby22
- It is possible to have a 16 bit datapath so the processor would have both 2 byte instructions and 2 byte data. This is limited to 64KB of memory, but that is enough for many applications
- The only change from baby42 is that immediate value -7 does not indicate a 32 bit immediate

---
Variation 2: baby042
- Operating on groups of 6 bits instead of 8 bit bytes we could have 24 bit data and 12 bit instructions. It is more natural to use octal instead of hexadecimal numbers
- With 4 fewer bits in each instruction it would be better to have 8 registers instead of 16. Instead of a dedicated immediate bit, when the second operand is register 6 or 7 the actual value is a 24 or 12 bit immediate after the instruction.
- 0XDS: d=s, , d=s+1, , d=!s, , d=~s,
- 1XDS: d+=s, {d+s}, d+=s+1, {d+s+s}, d-=s-1, {d-s-1}, d-=s, {d-s}
- 2XDS: d|=s, {d|s}, d^=s, {d^s}, d&=s, {d&s}, d!&=s, {d!&s}
- 3XDS: d>>=s, {d>>s}, d<<=s, {d<<s}, d$>>=s, {d$>>s}, d<>=s, {d<>=s}
- 4XDS: d>s?, {d>s}, d>=s?, {d>=s}, d==s?, {d==s}, d!=s?, {d!=s}
- 5TBS: ===> b[s]/t
- 6TBS: b[s] = t
- 7TBS: t = b[s]